## Slide 1: OKR04 Employee Training Requirements
GCSA Employee Training
Nienhuis Park Community Center
May 19, 2017
Richard Smith, Stormwater Consultant

## Slide 2
Searching OKR04
“Employee Training” requirements are not consolidated.
Must search all of OKR04 text using key words.
INCOG used: “train, employee, educate, inform, staff”.
Some “finds” referred to educating the public; INCOG’s training focuses on MS4 employees.
All employee training requirements are in Part IV (MCMs).
Some are “must do”; others are “recommendations”.
One “recommendation” not done often by INCOG requires local training of field workers – Part IV.3.b(5).

## Slide 3
OKR04 Employee Training Parts
OKR04 Part | Training Topics | Notes
IV.C.3.a(6) IDDE | Hazards associated with illegal discharges. | Requirement. Inform public employees about…
 | Improper disposal of waste. | 
IV.C.3.b(4) IDDE | Hazards associated with illegal discharges. | Recommendation; general public, employees and businesses.
 | Improper disposal of waste. | 
IV.C.3.b(5) IDDE | How to identify and report stormwater illicit discharges. | Recommendation; educate field workers such as in maintenance, building inspectors, etc.
IV.C.4.b(3) Construction | Requirements for inspection and enforcement of erosion and sediment control measures. | Recommendation; staff training

## Slide 4
OKR04 Employee Training Parts
OKR04 Part | Training Topics | Notes
IV.C.6.a Good House-keeping | about the operation and maintenance program... to reduce pollutant runoff… | Requirement; training component
IV.C.6.a(1) Good House-keeping | Park and open space maintenance. | Requirement; employee training to prevent and reduce stormwater pollution from...
 | Fleet and building maintenance. | 
 | New construction and land disturbances. | 
 | Stormwater system maintenance. | 
IV.C.6.a(2) Good House-keeping | Prevent and reduce stormwater pollution from MS4 activities. | Requirement; employee training to…

## Slide 5
OKR04 Interpretation
In the past, ODEQ has been generous in counting many types of learning experiences as employee training.
  Internal staff meetings discussing stormwater,
  Attending seminars, webinars, workshops, etc.
OKR04 does not define numbers, types, lengths, specific subjects or sources of training.
MS4s must keep records for Annual Reports.
INCOG tries to cover all OKR04-referenced topics, plus many more related and/or important to GCSA.

## Slide 6
Considerations for Future Training
Follow all requirements and advice from ODEQ.
Training will need to expand to field staff.
Maintain records on who, what, when, where.
Professional Certification programs:
  Are abundant, wide variety, most excellent quality.
  Are not offered or required by ODEQ or EPA.
  Most are costly, but many MS4 staff want credentials.
INCOG wants feedback on improving its training.

## Slide 7
Vernon Seaman
Manager, Envir. And Energy Planning
INCOG
Two West 2nd Street, Ste 800
Tulsa, OK 74103
(918) 579-9451
vseaman@incog.org
Questions ??